## Slide 1: Real Traffic Replay over WLAN with Environment Emulation 在無線區域網路中運用環境仿真的真實流量重播
Student: Pei-Hsuan Li
Advisor: Prof. Ying-Dar Lin
Date: 2011/6/3

## Slide 2: Outline
Motivation
  How does real traffic replay cooperate with environment emulation?
Background
Issues
  Controlling traffic behaviors
  Controlling environment factors
Related works
Problem statement
Solution approach
  Event-driven automata-synchronized replay(EDASR)
Implementation
Evaluation
Conclusion & future works
Reference

## Slide 3: Motivation
Real Traffic replay
  Using packet traces captured in real environments
    Variation and realism
      Trigger more problems
    Highly applied in wired networks
Issues of replay in wired networks
  Stateful packet replay control
    To manage interactions with DUTs
In wireless networks:
  Communication medium is open and shared
  Environment effects
    Packet exchange sequences may be disturbed
How to replay traffic cooperates with environment effects in wireless network
Notes: 真實流量提拱model不出的行為和複雜度
        Send out packets in the correct order and direction
wireless networks the environment effects have a strong impact on the data
communication,

## Slide 4: Background- Packet replay control
  To manage interactions with DUTs
    Follow the IEEE 802.11 protocol
      Station management entity
        Connection states
      Basic operation sequence
        Atomic operations
    Violating the protocol may result in invalid packet exchange sequences
Class 1
Notes:     short Inter-frame space
    positive acknowledgement

## Slide 5: Background- Environment effects
  The propagation signal is affected by following effects
    Fading
      Large scale
      Small scale
    Noise
      Different communication system
      Natural and manmade un-controlled signal
      Uses the same frequency channel
        Ex. Microwave
    Interference
      Based on 802.11
      Other devices using the medium at the same time
        Ex. Collisions
  Affect the originally bit stream could not be correctly demodulated and decoded
    High packet error rate
Notes:       Large scale
        Path loss caused by energy loss
      Small scale
        Shadowing caused by obstacles

## Slide 6: Issues of traffic replay in wireless networks
An efficient replay requests:
  Packet replay control& environment emulation
  Coordinate above elements
If any of the above conditions failed
  The reproduced traffic traces in the replay may suffer FN(False Negative) and FP(False Positive)
    FN
      Successful in the real environment
      Fails in the traffic replay
    FP
      Fails in the real environment
      Successful in the traffic replay
  Lose the realism of the real world action
Notes: Fading, interference and noise all may cause the signal cannot be demodulated and decoded into originally correct bit stream and cause the increase of bit error rate, which affects the packet error rate, too. So if we want to reproduce the real traffic behavior, we also need to reproduce the environment effects

## Slide 7: Lack the packet replay control
  FP: Affect the packet exchange sequence
    Transmit the next packet before receiving the response for the current request
  FN: Wrong interactions with the DUT
    Transmit the next packet at the wrong time
Captured traffic in the real world | 
A to B | Asso. Req.
B to A | ACK
B to A | Asso. Rep.
A to B | ACK
Captured traffic in the real world | 
B to A | Direct Data
B to A | Direct Data
B to A | Direct Data
A to B | ACK
Captured traffic in the real world | 
B to A | Direct Data
B to A | Direct Data
B to A | Direct Data
A to B | ACK
Notes: 因為

## Slide 8: Lack the environment emulation
  FN: Affect the packet exchange sequence
    Noise occurs too long
      Un-want disturbances
  FP: Wrong interactions with the DUT
    Noise did not occur
      Un-want responses from the DUT
Captured traffic in real world | 
A to B | Direct data(noise)
A to B | Direct data(noise)
A to B | Direct data(noise)
B to A | ACK(noise)
A to B | Direct data
B to A | ACK
Captured traffic in real world | 
A to B | Direct data
A to B | Direct data
A to B | Direct data
B to A | ACK
A to B | Direct data
B to A | ACK

## Slide 9: Lack the coordination
  FN: Affect the packet exchange sequence
    Noise occur at the wrong packet
      Un-want disturbances
  FP: Wrong interactions with the DUT
    Noise occur at the wrong packet
      Un-want responses from the DUT
Captured traffic in real world | 
A to B | Direct data(noise)
A to B | Direct data(noise)
A to B | Direct data
B to A | ACK
A to B | Direct data
B to A | ACK

## Slide 10: Related works
A number of studies investigated packet replay control and environment emulation issues
  Categories of Related works
    Model-based approaches:
      Utilize statistical methodologies
        Traffic patterns
        Environment effects
      Provide key parameters to configure
      Neglect complicated details
    Trace-based approaches:
      replay
        uses the real traffic traces and environment

## Slide 11: Categories of Related works
Issue | Type | Main idea | Extension
packet (reproduced) replay Control | Model-based | Use matrices to compute network behaviors | Workload patterns[3]
 |  | Multi-level of trafﬁc entities | IP trafﬁc model [4][5]
 | Trace-based | Bases on captured traffic and conﬁgurations | Selected traffic [6]
 |  | Traffic replay | Replay HTTP traffic[7]
environment emulation | Model-based | Get the deliver probability model | MAC and PHY model [8]
 |  |  | Use the SNR value [9]
 |  | Get the error probability model | Use trans. rate, data size, distance [10]
 |  | Use the user’s configuration | Model mobility[11][12]
 | Trace-based | Use different test scenarios | Changes the simulated environments by time [13]
 |  | Replay RSS value | By time stamp [14]
 |  | Attenuating the radio signals | large-scale-testbed and node mobility[15]
few previous studies considering both of
  packet replay control
  environment emulation
In this work, we develop a tool named EDASR to solve these problems.

## Slide 12: Problem statement- Notations and definitions
Because a single packet represents non meaningful behaviors
  Define events
    Refer to the protocol SPEC
      Represent meaningful packet exchange sequences
        Ex. RTS→CTS→Data→ACK
          Atomic event
        Ex. Assoc. req.->ACK->----Assoc. rsp.->ACK
          Non-atomic event
    A given packet trace could be transformed into a series of event
  Definitions of parameters
Parameter | Value | Description
 |  | the sequences of events captured in the real environment
 |  | the sequences of events reproduced by traffic replay
Parameter | Value | Description
 |  | the sequences of events captured in the real environment
 |  | the sequences of events reproduced by traffic replay

## Slide 13: Problem statement- Constraints and Variables
Given constraints
  Given the captured packets and corresponding environment information
Variables
  To partition the packets into a series of events
  To reproduce the captured packets with the corresponding environment information
    The results of replay is transformed into

## Slide 14: Problem statement- Objective
Objective
  Intend to make as consistent as possible with
    .
  To quantify the approximate level of traffic replay
    compares each event by the performance metric:
      Reproduction ratio
        is the number of events of

## Slide 15: Event-driven automata-synchronized replay(EDASR)- Overview
Capture:
  Record traffic traces at the transmitter
  Record env. factor at the receiver
Transform traffic into events:
  For evaluation
  For reply
      Replay event sequences
Replay:
  Coordination
    replay event sequences
    environment effects
Evaluate the capability of EDASR
    Use and
    Compute the reproduction ratio

## Slide 16: Capture traffic traces and environment effects
the variance of wireless communication systems
  The packets and environment effects
    Seen by the transmitter and the receiver could be different
    Record traffic traces at the transmitter
    Record env. factor at the receiver
Env. factor
traffic traces
Env. factor
traffic traces
Real environment
Replay
STA
    (transmitter)
AP
    (receiver)

## Slide 17: Transform traces into events
    Event analysis
      Follow the protocol
      Atomic events
        The following packets occupy the channel
      Non-atomic events
        DUT need to respond the request
      Atomic events
      Non-atomic
      events
Replay event sequence

## Slide 18: Reproduced by EDASR -Level-0 automata
      Use the automata of each event to control replay and synchronize the environment effects
  Level-0 automata
    Handling no event
    State transition triggered by
    atomic and non-atomic events
Replay event sequence
Env. effects

## Slide 19: Reproduced by EDASR- Level-1 automata
  Level-1 automata
    Handling non-atomic events
    State transition triggered by atomic events
Replay event sequence
Env. effects

## Slide 20: Reproduced by EDASR- Level-2 automata
  Level-2 automata
    Handling atomic events
    State transition triggered by packets
Replay event sequence
Env. effects

## Slide 21: Reproduced by EDASR- Event of three level automata

## Slide 22: Compute the reproduction ratio
According to the events
  Real environment:
  Traffic replay :
  Quantify the approximate level
    Reproduction ratio

## Slide 23: Reproduced by EDASR- Example
Capture traffic traces and environment effects
Transform into events
  For evaluation
  For reply
      Replay event sequences
      :
      {(DATA), (DATA ACK),}
      Replay event sequences:
      {(DATA ACK), (DATA ACK)}
Environment factors:
{-70,X,-60,-60}

## Slide 24: Reproduced by EDASR- Example(con.)
Replay:
  Coordination
    replay event sequences
    environment effects
Evaluate the capability of EDASR
    Use and
    Compute the reproduction ratio
Signal: -70dBm
Signal: Without change
      Replay event sequences:
      {(DATA ACK), (DATA ACK)}
Environment factors:
{-70,X,-60,-60}
Signal: -60dBm
Signal: -60dBm

## Slide 25: Reproduced by EDASR- Example(con.)
Transform traffic into events:
  For evaluation
Evaluate the capability of EDASR
    Use and
    Compute the reproduction ratio
      :
      {(DATA ACK), (DATA ACK),}
  = { 0, 1 }
  = { 1, 1 }
  Reproduction ratio = x100% = 50 %
      :
      {(DATA), (DATA ACK),}

## Slide 26: Implementation of EDASR
Architecture of EDASR on the Linux
AP

## Slide 27: Evaluation
Use the reproduction ratio to evaluate the performance of EDASR
  The packet replay control
    Atomic events
    Non-atomic events
  The environment emulation
    Signal
    Noise
    Interference
    0
    0
  Parameters of the environment emulation
Parameter Name | Value
Traffic trace | IPTV traffic (total 7500000byte)
Signal strength | -64dBm
Noise strength | -85dBm
Interference period | 40000us
Interference strength | -69dBm
Parameter Name | Value
Traffic trace of atomic events | Data event
Traffic trace Non-atomic events | Probe event
  Parameters of the packet replay control

## Slide 28: Evaluation- Capture traffic and environment effects
  The experiment of the packet replay control
  The experiment of the environment emulation
Talk
Talk
Talk
Talk
Listen
Listen
Listen
Listen

## Slide 29: Evaluation- Replay
With EDASR
Without EDASR
  Without packet replay control
  Without environment emulation
Talk
Talk
Listen
Listen
Talk
Talk
Listen
Listen

## Slide 30: Traffic behavior control- Non-atomic events
Chart: Reproduction Ratio (%)
| 20 | 40 | 60 | 80 | 100
Without traffic control replay | 84.2 | 68.21 | 52.81 | 36.55 | 20.68
EDASR | 99.17 | 98.67 | 97.91 | 98.85 | 98.92
Non-atomic events/total events x 100%
Reproduction Ratio (%)
Keep the waiting time between request and response
Without packet-replay
control

## Slide 31: Traffic behavior control- Atomic events
Chart: 
| 20 | 40 | 60 | 80 | 100
Without packet replay control | 99.85 | 99.975 | 99.9167 | 99.6625 | 99.96
EDASR | 99.65 | 99.6 | 99.9333 | 99.975 | 99.96
Reproduction ratio(%)
Atomic events/total event x 100%
The speed of replay is not fast enough to interrupt the atomic events

## Slide 32: Environment emulation- Signal fading
Chart: 
| -59 | -64 | -69 | -74 | -79 | -84
Without environment emulation | 96.1012 | 97.3903 | 92.2235 | 0.010435 | 0 | 0
EDASR | 96.0712 | 97.3903 | 92.4545 | 99.0817 | 99.6648 | 100
Reproduction Ratio (%)
Signal strength(dBm)
  Consider the un-ideal wireless environments
      and could be 0 or 1 based on the packet error rates
The probability of bit error
is affected by the SNR
SNR
BER

## Slide 33: Environment emulation- Noise
Reproduction Ratio(%)
Chart: 
| -85 | -60 | -50 | -40 | -30 | -20
Without environment emulation | 97.3903 | 96.0184 | 88.5162 | 0 | 0 | 0
EDASR | 97.3903 | 96.0284 | 88.7064 | 99.597 | 99.7981 | 99.4641
Noise strength(dBm)
Notes: CAMA/CA:節點會檢查是否有其他的節點正和存取點通訊, 如果有,節點會先等待一段random時間, 再試著傳送,以免再傳送時又發生碰撞 collision

## Slide 34: Environment emulation- Interference
Chart: 
| -59 | -49 | -39 | -29 | -19 | -9
Without environment emulation | 99.4175 | 99.4004 | 98.1226 | 99.2696 | 99.2253 | 99.0829
EDASR | 99.4175 | 98.6789 | 98.133 | 98.7319 | 98.9908 | 99.0829
Interference signal strength(dBm)
Reproduction Ratio (%)
Collision Avoidance
Use CAMA/CA to avoid collision
CCA

## Slide 35: Conclusion
EDASR provides a solution:
  Replay traffic cooperates with environment effects in wireless network
    Under DUT-dependent traffic
      Reproduction ratio: over 95.9%
    Under the un-ideal wireless environment
      Reproduction ratio: over 88.7%
  Without EDASR
    Under DUT-dependent traffic
      The worst case of the reproduction ratio: only 20.68%
    Under the un-ideal wireless environment
      The worst case of the reproduction ratio: only 0%
Main idea of EDASR :
  Define events
  Using the automata of each event to control the replay
    Replay traffic cooperates with environment effects

## Slide 36: Future works
Our software implementation has proven that EDASR is useful
Next steps:
  Implement EDASR into kernel level
    Decrease the overhead of context switch(because)
      Increase the replay performance
        Support the high speed packet(Ex. ACK) transition
        Support the high data transition rate
          Use different moderations
    Methods:
      Kernel module
      Modify driver

## Slide 37: References
[1] Wu-Chang Feng, Ashvin Goel, Abdelmajid Bezzaz, and Wu-Chi Feng, “TCPivo: a high-performance packet replay engine,” Jonathan Walpole, in Proceeding MoMeTools '03 Proceedings of the ACM SIGCOMM workshop on Models, methods and tools for reproducible network research, 2003.
[2] Tsung-Huan Cheng, and Ying-Dar Lin, “Low-Storage Capture and Loss-Recovery Stateful Replay of Real Flows,” Univ. National Chiao Tung, HsinChu, Taiwan, Tech. Rep., Jun. 2009.
[3] Stefan Karpinski, Elizabeth M. Belding, Kevin C. Almeroth, and John R. Gilbert, “Linear Representation of Network Traffic,” Journal Mobile Networks and Applications, Volume 14 Issue 4, 2009.
[4] Chloé Rolland, Julien Ridoux, and Bruno Baynat, “LiTGen, a Lightweight Traﬃc Generator:Application to P2P and Mail Wireless Traﬃc,” in Proceedings of PAM'07 Proceedings of the 8th international conference on Passive and active network measurement, Apr. 2007.
[5] Chloé Rolland, Julien Ridoux, Bruno Baynat, and Vincent Borrel, “ Using LiTGen, a realistic IP traffic model, to evaluate the impact of burstiness on performance,” in Proceeding Simutools '08 Proceedings of the 1st international conference on Simulation tools and techniques for communications, networks and systems & workshops, 2008.
[6] Caleb Phillips, and Suresh Singh, “Techniques for Simulation of Realistic Infrastructure Wireless Network Traffic, ” Modeling and Optimization in Mobile, Ad Hoc, and Wireless Networks, 2009. WiOPT 2009. 7th International Symposium on, Jun. 2009.
[7] Ming Wan, Nan Yao, Ying Liu, and Hongke Zhang, “A fast information reproduction method for HTTP in WLAN,” Wireless Communications, Networking and Information Security, 2010 IEEE International Conference on , pp. 365 - 369 ,Jun. 2010.

## Slide 38: References
[8] Vincent Lender, and Margaret Martonos, “Repeatable and Realistic Experimentation in Mobile Wireless Networks,” IEEE Transactions on Mobile Computing, vol. 8, no. 12, Dec. 2009.
[9] Charles Reis, Ratul Mahajan, Maya Rodrig, David Wetherall, and John Zahorjan, “Measurement-Based Models of Delivery and Interference in Static Wireless Networks,” in Proceeding SIGCOMM '06 Proceedings of the 2006 conference on Applications, technologies, architectures, and protocols for computer communications, 2006.
[10] Giao T. Nguyen, Randy H. Katz, and Brian Noble, Mahadev Satyanarayanan, “A trace-based approach for modeling wireless channel behavior,” in Proceeding WSC '96 Proceedings of the 28th conference on Winter simulation, 1996.
[11] Pei Zheng, and Lionel M. Ni,“EMWIN: Emulating a Mobile Wireless Network using a Wired Network”, WOWMOM '02 Proceedings of the 5th ACM international workshop on Wireless mobile multimedia, 2002.
[12] Pei Zheng, and Lionel M. Ni ,”EMPOWER: A Network Emulator for Wireline and Wireless Networks,” INFOCOM 2003. Twenty-Second Annual Joint Conference of the IEEE Computer and Communications. IEEE Societies, Apr. 2003.
[13] Markku Kojo, Andrei Gurtov, Jukka Manner, Pasi Sarolahti, Timo Alanko, and Kimmo Raatikainen, “Seawind: A wireless network emulator,” in Proceedings of 11th GI/ITG Conference on Measuring, Modeling and Evaluation of Computer and Communication Systems, 2001.
[14] Glenn Judd, and Peter Steenkiste, “A simple mechanism for capturing and replaying wireless channels,” in Proceedings of the 2005 ACM SIGCOMM workshop on Experimental approaches to wireless network design and analysis, 2005.

## Slide 39: References
[15] Pradipta De, hshish Raniwala, Srikant Sharma, and Tzi-cker Chiueh, “Mint: A miniaturized network testbed for mobile wireless research,” INFOCOM 2005. 24th Annual Joint Conference of the IEEE Computer and Communications Societies. Proceedings IEEE, Mar. 2005.
[16] P. Brenner, “A Technical Tutorial on the IEEE 802.11 Protocol,” BreezeCom, Jul. 18, 1996.
[17] Matthew S Gast, 802.11 Wireless Networks: The Definitive Guide, Second Edition, O'Reilly Media, Inc., 2005.
[18] OmniPeek Network Analyzer, http://www.wildpackets.com
[19] Libpcap, http://www.tcpdump.org
[20] E-INSTRUMENT TECHEPA-1200B, http://e-channel.com.tw/
[21] Agilent Technologies, http://www.home.agilent.com
[22] NI-488.2 library, http://www.ni.com

## Slide 40
Multi state-machine
Multi-level