## Slide 1: Identifying and Downsizing Packet Traces Triggering Defects in Networking Devices
Student: P. Eliézer Zongo (鍾艾利）
Advisor: Dr. Ying-Dar Lin
Date:08/06/2012
MASTER THESIS

## Slide 2: OUTLINE
Background
  Testing of Networking Devices
Motivations
  Related Works
    Overview of In-Lab Replay Testing (ILRT)
Problem Statement
Solution Approach
  Linear Downsizing (LD)
  Binary Downsizing (BD)
Evaluation & Observations
  Defects Distribution
  Downsized Ratio
  Replay Throughput vs. Defects Occurrence
  Case Study: Investigating causes of defects
Conclusions and Future Work
References

## Slide 3: Background
Why Testing Networking Devices?
  Discover and fix devices defects
  Reduce number of customers found defects
  Enhance devices robustness
Replay as Testing Technique
  Artificial Traffic
  Real Traffic
    Realistic properties
    Diversity & Complexity (applications & Protocols)
    Proprietary protocols hard to model in Lab (P2P, video streaming, gaming…)

## Slide 4: Motivations(1)
Testing devices with real traffic is challenging:
  High volume of captured traces (ie.120 GB/hour in NCTU Beta Site)
  Storage of traces
  Time-consuming process
    The replay of 2TB of traces requires 120 hours
    Traces downsizing is essential to improve testing efficiency

## Slide 5: Motivations(2)
Traces downsizing is not trivial
  Some issues
    Defect Reproduction
    Reduced Testing Time
    Storage: reduce volume of traces
  Downsized traces should be representative of raw traces.

## Slide 6: Related Works (1) Overview of In-Lab Replay Testing (ILRT)
NCTU Beta Site
NBL: Network Benchmarking Lab
DUT: Device Under Test
ILRT Architecture

## Slide 7: Related Works (2) “Bug Traces” Collection Process
n = 2
  “Bug traces”: traces that have triggered some defects of devices during test.

## Slide 8: Related Works (3)
Related Works | Type of traces | Defect-based | Objective | Source of Traces | Method
Entropy-Based Reduction, | Offline | No | Off-line approach for reducing large data set applied to gaming traces Improve Analysis and Storage | Counter-strike game | Removal of data with redundancy at packet level Characterization and Modeling of network traffic
Reducing Network Traffic Data Sets |  |  |  |  | 
Network Trace Compression, | On-line | No | Low bandwidth communication | unknown | Compression of packet headers Prediction: 25% compression
Our work | Offline | Yes | Defect-driven packet Traces downsizing | Real traffic | Linear & Binary Downsizing method using replay technique

## Slide 9: Problem Statement (1)
Notation Table

## Slide 10: Problem Statement (2)
  Given
  A set of captured packet traces {Pj , j=1...m} and
  A set of devices defects in terms of logs {Li , i=1…n}
  Objectives
  Traces Identification
  Traces Downsizing

## Slide 11: Solution Approach
Overview of General Solution Approach

## Slide 12: Linear Downsizing
Rollback-and-replay
Replay in a decreasing order
Set incremental size (S)

## Slide 13: Linear Downsizing
Linear Downsizing Process
+
DUT
✔
✖
+
+
+
✔
Downsized traces
+
Incremental
Notes: Change to pseudo-code

## Slide 14: Binary Downsizing
Based on Binary Search Algorithm
PR
PLLL
PLLR
PLRL
PLRR
PRLL
PRLR
PRRL
PRRR
PLL
PLR
PRL
PRR
PL
Notes: Based on BD algorithm
Divide traces in 2 halves
Pick the right-half
replay to DUT
  If defect is triggered  divide
  Else include the right half of the previous left
Change to Pseudo-Code
----- Meeting Notes (5/31/12 14:15) -----
PSEUDOCODES

## Slide 15: Evaluation
Experiments Environment
Defects Distribution
Downsizing Ratio
Replay Throughput vs. Defects
Causes of Defects (Case Study)

## Slide 16: Sample Traces
Number of traces: 34

## Slide 17: Overview of Defects
7 types of defects
Single-defects (3)
Combined-defects (3)
Hanging(1)

## Slide 18: Defects Distribution (1)
ICMP & HTTP defects represent more than half (60%) of the total number of defects produced by DUTs
ICMP and HTTP requests are more resource-intensive (more overhead to DUT) than ARP requests
DUT Self-protection
Chart: Overall defects differentiation
| ARP | HTTP | ICMP | ICMP/HTTP | ARP/ICMP | ARP/HTTP | Crash
 | 0.10345 | 0.31034 | 0.27586 | 0.17241 | 0.034483 | 0.034483 | 0.068966

## Slide 19: Defects Distribution (2)
The number of defects per DUT reflects that of the overall defects distribution
Chart: 
| ARP | HTTP | ICMP | ICMP/HTTP | ARP/ICMP | ARP/HTTP | crash
DUT1 | 0.1667 | 0.5 | 0.5 | 0.1667 | 0.11 | 0.12 | 0.1667
DUT2 | 0.29 | 0.45 | 0.4 | 0.32 | 0.09 | 0.08 | 0.19
DUT3 | 0.22 | 0.2857 | 0.7 | 0.2857 | 0.1429 | 0.05 | 0.2
DUT4 | 0.2 | 0.35 | 0.8 | 0.32 | 0.07 | 0.11 | 0.16
Defects
Types of Defects

## Slide 20: Sample of Downsized Traces
DUT / DEFECT | DUT1 (✔) |  |  | DUT2 (✔) |  |  | DUT3 (✔) |  |  | DUT4 (✔) |  | 
 | DUT2 | DUT3 | DUT4 | DUT1 | DUT3 | DUT4 | DUT1 | DUT2 | DUT4 | DUT1 | DUT2 | DUT3
Hanging | 0.96 GB |  |  | 326.35 GB |  |  | 27.35 GB |  |  | 1200 GB |  | 
 | ✖ | ✖ | ✖ | ✔ | ✔ | ✖ | ✔ | ✖ | ✖ | ✔ | ✔ | ✔
ICMP | 0.96 GB |  |  | 7.7 GB |  |  | 15.32 GB |  |  | 24.1 GB |  | 
 | ✖ | ✖ | ✖ | ✔ | ✔ | ✖ | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
HTTP | 0.96 GB |  |  | 0.63 GB |  |  | 10.38 GB |  |  | 20.96 GB. |  | 
 | ✔ | ✖ | ✖ | ✖ | ✖ | ✖ | ✔ | ✔ | ✖ | ✔ | ✔ | ✔
✔: defect ✖: No defect
Downsized traces also trigger defects on multiple DUTs as it is the case for the “bug traces”.

## Slide 21: Downsizing Ratio
Evaluation Metrics - Formulas
(1)
(2)
: Size of downsized trace that triggered a defect Li
: Size of a non-downsized packet
|P|: Original Packet Trace

## Slide 22: Comparison of Two DR Evaluation Methods
DR2 is slightly higher than DR1
DR2 is function of the size of raw packet traces P unlike DR1
Chart: Downsizng Algorithm
| BD | LD
DR1 | 0.735 | 0.78
DR2 | 0.8 | 0.825

## Slide 23: Comparison of Two DR Algorithms
Using BD and LD algorithm, a DR of 77% and 80% are achievable.
DR of LD is slightly higher than that of BD because traces triggering the defects are contained in about 17% of the traces replayed before the defect occurrence.
Chart: Downsizing Algorithm
| BD | LD
 | 0.77 | 0.8

## Slide 24: Performance of LD and BD
Downsizing Processing Time: LD is 3.1 times slower than BD
Testing Iterations: LD requires about 5 times more iterations than BD
Chart: 
| Replay Time | Iteration
BD | 0.31951 | 0.2
LD | 1 | 1
%

## Slide 25: Illustration of BD
8047
4024
Original Trace size: 1.2 TB
8047 MB
✔
4024
2012
2012
✔
✔
1006
1006
✖
1006
503
✖
1006
503
251
✔
1006
503
126
126
✔
1006
503
63
63
✔
1006
503
32
32
✖

## Slide 26: Illustration of LD
500 | 500 | 500 | 500 | 500 | … | 500 | 47
47
500
47
500
47
500
500
47
500
500
✖
✖
✖
✔
47
547
1047
1547
8047
(16*500 +47)
Original Trace size: 1.2 TB
8047 MB
✔: defect ✖: No defect

## Slide 27: Replay Throughput and Defects(1)
Networking devices produce 1.5 – 2.8 times more defects with higher replay throughput (100 mbps) than in lower replay throughput (50mbps).
Chart: Defect Type
| ARP | HTTP | ICMP | ICMP/HTTP | ARP/ICMP | ARP/HTTP | Crash
50 mbps | 0.024691 | 0.11111 | 0.098765 | 0.061728 | 0.012346 | 0.012346 | 0.024691
100 mbps | 0.049383 | 0.19753 | 0.14815 | 0.17284 | 0.024691 | 0.024691 | 0.037037

## Slide 28: Replay Throughput and Defects(2)
Replay Throughput | Round 1 | Round 2 | Round 3 | Round 4
25 mbps | ✖ | ✖ | ✖ | ✖
37.5 mbps | ✖ | ✖ | ✖ | ✖
50 mbps | ✔ | ✔ | ✔ | ✔
62.5 mbps | ✔ | ✔ | ✔ | ✔
75 mbps | ✔ | ✔ | ✔ | ✔
87.5 mbps | ✔ | ✔ | ✔ | ✔
100 mbps | ✔ | ✔ | ✔ | ✔
In some cases, defects are not triggered below 50 mbps. Number of requests per time unit is more likely to increase with higher replay throughput.
✔: hanging ✖: No hanging

## Slide 29: Case Study: Investigation of Defects Causes
Black-box Testing
Analysis through open source firmware
Based on ILRT inventory (only DUT4 supports Open source firmware )
Experiment using same variables
  Same environment
  Packet traces
  Replay throughput
Notes: SOHO Router is a black-box device
No significant output (information)
  Installed an OpenSource Firmware (DD-WRT) on a ASUS RT-N16. (it only support/compatible unlike others )
  Replayed with same packet traces that triggered failure (crash) on other devices
Results

## Slide 30: Hanged DUT Log Message
Log message from (/var/log/messages)
Saturation of the DUT’s connection tracking table due to high number of incoming packets.

## Slide 31: Failed DUT Status
CPU and Connection Status from DUT Web Interface
CPU: High usage
Exhaustion of number of available connections and ports

## Slide 32: Reasons of NAT Table Exhaustion
Insufficient capacity of NAT table net.ipv4.ip_conntrack_max
  Default: 4096 entries
High "Established Connection" timeout time: ip_conntrack_tcp_timeout_established = 5 days

## Slide 33: Conclusions
Defect Differentiation
  7 types of observed defects with ICMP and HTTP defects representing more than half (60%) of total defects.
Downsizing Ratio
  Downsizing Ratio: 77% (BD) and 80% (LD)
  Downsizing Processing Time: LD is 3.1 times slower than BD
  Number of Iterations: LD requires about 5 times more iterations than BD
Replay Throughput and Defects
  DUTs are more likely to produce more defects when tested in higher replay throughput (1.5 – 2.8 times more defects)
Possible Defects Causes:
  Size of NAT Table
  DUT’s Failure to handle more active Connections

## Slide 34: Future Works
Introducing more probing techniques in order to figure out DUTs internal defects and performance
Evaluating defects not related to DUTs’ ability to respond to status query requests

## Slide 35: References (1)
Y. D. Lin, I. W. Chen, P. C. Lin, C. S. Chen, C.H. Hsu, “On Campus Beta Site: Architecture Designs, Operational Experience, and Top Product Defects,” IEEE Communication Magazine, 2010
M. K. Daskalantonakis, “A Practical View of Software Management and Implementation Experiences within Motorola,” IEEE Trans. Software Eng., vol. 18, no. 11, 1992, pp. 998–1009.
Alessio Botta, Alberto Dainotti, Antonio Pescape, and Giorgio Ventre “Reducing Network Traffic Data Sets” ICC 2007 proceeding
“Entropy-Based Reduction of Traffic Data”, IEEE Communications Letters, Vol.11, No.2, February 2007.
Y. Liu, D. Towsley, J. Weng, D. Goeckel, “An Information Theoretic Approach to Network Trace Compression”, UM-CS-2005-003 TR, Jan 2005
Y. Liu, D. Towsley, T. Ye, and J. Bolot, “An Information-theoretic Approach to Network Monitoring and Measurement” IMC 2005
G. Iannaccone, C. Diot, I. Graham, and N. McKeown. “Monitoring very high speed links,” Proceedings of ACM Internet Measurement Workshop, November 2001.
M. Peuhkuri. “A method to compress and anonymize packet traces,” Proceedings of ACM Internet Measurement Workshop, November 2001.
Y. Liu, D. Towsley, T. Ye, and J. Bolot, “An Information-theoretic Approach to Network Monitoring and Measurement,” IMC 2005
K. C. Claffy, G. C. Polyzos, and H. W. Braun, “Applications of Sampling Methodologies to Network Traffic Characterization,” ACM SIGCOMM

## Slide 36: References (2)
K. C. Claffy, G. C. Polyzos, and H. W. Braun, “Applications of Sampling Methodologies to Network Traffic Characterization,” ACM SIGCOMM
Szabó, G., Szabó, I., Orincsay, D “Accurate Traffic Classification,” IEEE WOWMOM, Finnland, June 2007
Karagiannis, T., Papagiannaki, K., Faloutsos, M “BLINC: Multilevel Traffic Classification in the Dark”, ACM SIGCOMM, Philadelphia, USA, August 2005
NBL PCAPLib. [Online]. Available: http://security.nbl.org.tw/
Y-D. Lin, T.-H. Cheng, P.-C. Lin, I.-W. Chen, and Y.-C. Lai,“Low-storage capture and loss-recovery stateful replay of real flows,” IEEE Communications Magazine, to appear, available upon request.
Ying-Dar Lin, Jui-Tsun Hung, Ren-Hung Hwang, Chun-Nan Lu “In-Lab Live Testing with A Case Study on SOHO Routers”
TCPReplay.[Online].Available: http://tcpreplay.synfin.net/
Network Benchmarking Lab.[Online].Available: http://nbl.org.tw
Binary Search Algorithm.[Online].Available: http://en.wikipedia.org/wiki/Binary_search_algorithm
Netfilter.[Online].Available: http://www.netfilter.org

## Slide 37
THANK YOU