## Slide 1
OFBench: Performance test suite on OpenFlow switches
Student: Chen-You Wang 學生：王辰佑
Advisor: Ying-Dar Lin 指導教授：林盈達
Design Guidelines:
Propose 5 test cases to evaluate the switches.
Test 7 performance parameter: action time, pipeline time, buffer size, packet-in rate, packet-out rate, pipeline gain and timeout accuracy.
Automatic test framework with controller-agent architecture.
Packet-in / Packet-out rate
Pipeline gain
Conclusion:
Hardware switches have ±20% idle-timeout deviation.
Hardware switches are capable of generating Packet-in frames in the rate ranging from 3000 to 7000 pps .
Hardware switches have better pipeline gain which ranging from 40 to 60%.
國立交通大學 網路工程研究所
Switch | Idle-timeout | Hard-timeout
Open vSwitch | 2% | 0%
Pica8 P-3290 | -16.24% | 4.7%
Pica8 P-3297 | 24.64% | 3.3%
Edge-corE AS4610 | 10% | 0%
Centec V350 | 17.64% | 1.66%
Action time
Timeout accuracy