## Slide 1: OFBench: Performance test suite on OpenFlow Switches
Author: Chen-You Wang
Advisor: Dr. Ying-Dar Lin
Affiliation: NCTU
Date: 2016/06/03

## Slide 2: Outline
Motivation
Background
  OpenFlow
  OpenFlow Instructions
  OpenFlow Performance Parameters
Issues
Survey
  Traditional Data Plane
  OpenFlow Data Plane
  Bidirectional
Problem statement
Approach
  Mirror-in-progessing
  Calculated traffic
  Masked entry
Implementation
Experiment and results
Conclusion
Future work
Reference

## Slide 3: Motivation
Open Network Foundation (ONF) [1]
OpenFlow[2] switch
  Conformance: OFTest[3], Ryu certification[4]
  Performance
switch
control plane
data plane
controller
control plane
switch
data plane
control plane triggering
data plane (C2D)
data plane triggering
control plane (D2C)
Notes: 原因？與別人有什麼不同？別人缺了什麼？
抽離 control plane，以往的 performance 測試測不到純 control plane 的部分
但多了 control plane to data plane 的測試類別
而原本傳統網路的 data plane to control plane 還是存在，但機制上的不同需特地處理
而 data plane 的部分，除了傳統的部分外，因應 SDN 彈性化的需求，導致標準的 data structure 產生，最終需要對應的 Test case => OpenFlow data plane

## Slide 4: Background - OpenFlow
Open Network Foundation (ONF) [1]
Standard communications interface.
  Separate control plane and data plane.
  Flow entry
Attributes | Matches | Instructions
priority=1, timeout=5 | in_port=1,eth_src,ip_src | write_actions=output:2

## Slide 5: Background - OpenFlow Instructions[2]
Instructions list order by execution order:
Meter
Apply-Actions
  Applies the specific action(s) immediately without change the action set
Clear-Actions
Write-Actions
Write-Metadata
Goto-Table

## Slide 6: Background - OpenFlow Performance Parameters (1/3)
Control plane triggering data plane (C2D)
Data plane triggering control plane (D2C)
Data plane
  Traditional (TD)
  OpenFlow (OFD)
Controller
OF Switch
C2D
D2C
TD
OFD

## Slide 7: Background - OpenFlow Performance Parameters (2/3)
C2D
  Flow-mod
  Packet-out
D2C
  Packet-in
Controller
OF Switch
Flow-mod
Packet-in
Packet-out

## Slide 8: Background - OpenFlow Performance Parameters (3/3)
TD
  Latency
  Loss
  Buffer size
  Throughput
  Jitter
OFD
  Table lookup
  Multiple table pipeline
  Action
  Timeout
  Table size

## Slide 9: Issues
How to test the OFD, D2C, C2D parameters.
Black-box test for some internal parameter.
Notes: Some matrix behind process.

## Slide 10: Survey - Traditional Data Plane
Parameter | Bianco [7] | Emmerich [8] | Gelberger [9] | Jarschel [10]
Latency | ✓ | ✓ | ✓ | N/A
Loss | ✓ | N/A | N/A | N/A
Buffer size | N/A | N/A | N/A | ✓
Throughput | ✓ | ✓ | ✓ | ✓
Jitter | N/A | N/A | ✓ | N/A

## Slide 11: Survey - OpenFlow Data Plane
Type | Parameter | Spirent [5] | OFLOPS [6] | Bianco [7] | Ours
OFD | Table Lookup | Concept | N/A | Constant | N/A
 | Table Pipeline | Concept | N/A | N/A | Time, pipeline gain
 | OpenFlow Action | N/A | End-to-end | N/A | Exactly action time
 | Timeout | Concept | N/A | N/A | Accuracy
 | Table Size | Concept | N/A | N/A | N/A

## Slide 12: Survey - Bidirectional
Type | Parameter | Spirent [5] | OFLOPS [6] | Bianco [7] | Handfield [12] | Ours
D2C | Packet-in rate | Concept | N/A | N/A | N/A | Buffer size
C2D | Packet-out rate | Concept | N/A | N/A | N/A | Buffer size
 | Latency of Flow-mod | N/A | Traffic validation | N/A | Impact factors | N/A

## Slide 13: Problem statement - Notations(1/2)
Category | Notation | Description
Entity | c | The controller
 | dut | The switch under test.
 | N | The number of tables for dut.
 | H = {hn ¦ n ≧ 2} | The set of hosts.
 | CAP = {capc, capn ¦ n ≧ 2} | The set of link capacities. capc / capn is link capacity between c / hn and dut.
C2D | CD = POR | The parameter for C2D. POR means the throughput of packet-in operation in dut.
D2C | DC = PIR | The parameter for D2C. PIR means the throughput of packet-in operation in dut.
OFD | Taction-set | The time of action set execution in dut.
 | Ttable-pipeline | The time of table pipeline in dut.
 | buf | The size of buffer in dut.

## Slide 14: Problem statement - Notations(2/2)
Category | Notation | Description
OFD | Acchard-timeout, Accidle-timeout | The accuracies of hard-timeout and idle-timeout in dut.
 | P | The gain of table pipeline in dut.
 | Dopenflow | Dopenflow = {Taction_set, Ttable_pipeline, Acctimeout, P} The set of parameters for OpenFlow data plane triggering data plane.
Process | TB = {tablei ¦ 0 < i ≦ N} | The set of flow tables in dut.
 | F = {flowi,j ¦ 0 < i ≦ N, j > 0} | The set of flow entries. flowi,j mean the flow entry in tablei
 | TFC = {tfcy ¦ y > 0} | The set of traffics which be sent from src to dst. src ∈ H, dst ∈ H. tfcy = {pktz ¦ z > 0}
 | Ttable_lookup | The time of looking up the flow table in dut
 | Tapply_action | The time of executing Apply-Action in dut.
 | Tidle-timeout, Thard-timeout | The timeout value for idle/hard timeout flow entry.
 | Tidle-expired, Thard-expired | The arrival time of flow-removed message for idle/hard timeout flow entry at c
 | Tidle-duration, Thard-duration | The duration of flow-removed message for idle/hard timeout flow entry.

## Slide 15: Problem Statement
Given:
  the controller c
  the set of hosts H
  the switch under test dut
  the number N of tables for dut
  the set of link capacities CAP
Objectives:
  determine F, TFC
    most accurate CD, DC, Dopenflow
Constraints:
  dut not be modified

## Slide 16: Problem Statement - Example

## Slide 17: Approach - Overview
Category | Test Case | Method | Parameters | Output
Mirror-in-processing | Action set | Mirror-first-then-action | OpenFlow action | Taction-set
 | Pipeline time | Mirror-first-then-pipeline | table pipeline | Ttable_pipeline
Calculated traffic | Buffer size | Burst-until-loss | buffer size, packet-in rate, packet-out rate | buf, PIR, POR
 | Pipeline gain | Back-to-back-traffic | table pipeline | P
Masked entry | Timeout accuracy | Idle-timout-derived-by-hard-timeout | timeout | Acchard-timeout, Accidle-timeout
Notes: Non-trivial: 7
Ours: 6
Others: 1
Trivial: 6

## Slide 18: Approach - Action set (1/5)
Mirror-first-then-action
Input: tfcy, F
Output: Taction-set
α = time of pktz arrival
β = time of pktz’ arrival
Taction-set = β - α
end-to-end
action time
Notes: 考量情境並說明情境

## Slide 19: Approach - Pipeline time(2/5)
Mirror-first-then-pipeline
Input: tfcy, F
Output: Ttable-pipeline
RTT = ( pktz / capn ) * 2
T1 = Ttable_lookup + Tapply_action + RTT
T2 = Ttable-pipeline + Ttable_lookup + Tapply_action+ RTT/2
Ttable-pipeline = T2 - T1 + RTT/2

## Slide 20: Approach - Buffer size (3/5)
Burst-until-loss
Input: tfcy, N, T
Output: buf, PIR, POR
m < n
buf = m * pkt
PIR = n / T1
POR = m / T2

## Slide 21: Approach - Pipeline gain (4/5)
Back-to-back-traffic
Input: tfcy, F, n, z
Output: P
P = Tpkt / (Tbubble + Tpkt)
(b) Without pipeline
(a) Full pipeline
Tbubble

## Slide 22: Approach - Pipeline gain (4/5)
Back-to-back-traffic
Input: tfcy, F, n, z
Output: P
P = Tpkt / (Tbubble + Tpkt)
Tpkt ≅ Tinit / (n + 1)
Tbubble + Tpkt ≅ (T - Tinit) / n
αz = time of sending pktz
βz = time of pktz arrival
T = βn+1 - α1
Tinit = β1 - α1

## Slide 23: Approach - Pipeline performance (4/6)
T
T
Without pipeline
Pipeline
Ppipeline ≒ 33.3 %
Δt
Δt
Ppipeline ≒ 60 %
Δt
T
Notes: pipeline 獲益
T_init + (n - 1) *

## Slide 24: Approach - Timeout accuracy (5/5)
idle-timeout timer resetting
Idle-timout-derived-by-hard-timeout
hard-timeout=5
10s
idle-timeout=5
5s
10s

## Slide 25: Approach - Timeout accuracy (5/5)
T1
Timer synchronization | 
Time | F
T1 | idle-timeout=10, idle-age=0, priority=1, tcp, actions=output:1
T2 | idle-timeout=10, idle-age=0, priority=1, tcp, actions=output:1
 | hard-timeout=10, hard-age=0, priority=2, tcp, actions=output:2
T2 + 1 | idle-timeout=10, idle-age=1, priority=1, tcp, actions=output:1
 | hard-timeout=10, hard-age=1, priority=2, tcp, actions=output:2
T2

## Slide 26: Approach - Timeout accuracy (5/5)
Idle-timout-derived-by-hard-timeout
Input: tfcy, F
Output: Acctimeout
Tidle-timeout = Thard-timeout
α = time of pktz arrival, β = time of pktz' arrival
Tidle-forward = αn - α1
Thard-forward = βz - βn+1
Tidle-expired ≦ Thard-expired
  Acchard-timeout = Thard-forward - Thard-timeout Accidle-timeout = Tidle-duration - Tidle-forward - Tidle-timeout
(a) Tidle-expired ≦ Thard-expired

## Slide 27: Approach - Timeout accuracy (5/5)
Idle-timout-derived-by-hard-timeout
Tidle-expired > Thard-expired
  Increase Thard-timeout
  Reset hard-timeout flow entry
(b) Tidle-expired > Thard-expired

## Slide 28: Implementation
Tools
  OF controller: Ryu v3.2.1
  Traffic generator: Ostinato v0.7
  Software switch: Open vSwitch v2.3.2
OFBench architecture
  test cases
  hosts with agent
    traffic generator, parsing
Component | core | clock rate | OS | kernel
Controller | 4 | 3.3 GHz | Ubuntu 14.04 | 3.13.0-24
Host | 4 | 3.2 GHz | Ubuntu 14.04 | 3.13.0-24
Switch | 2 | 3.1 GHz | Ubuntu 14.04 | 3.13.0-24

## Slide 29: Experiment
Testbed
Configuration
  pkt: frame size, transmission rate
  switch: hardware, software
Issues to study
  Effect of different configuration

## Slide 30: Switch Specifications
Switch | CPU | core | clock rate | Memory | buffer | OS version
Pica8 P-3290 | MPC8541 | 1 | 1 GHz | 512 MB | 4 MB | v2.6.1
Pica8 P-3297 | P2020 | 2 | 1.33 GHz | 2 GB | 4 MB | v2.6.1
Edge-corE AS4610-30T | ARM Cortex A9 | 2 | 1 GHz | 2 GB | N/A | v2.6.4
Centec V350 | e500v2 | 1 | 533 MHz | 2 GB | N/A | v3.1(11), 1.alpha

## Slide 31: Traffic generator

## Slide 32: Results - Action time
packet-per-sec: 1000
duration: 10s
eth
ip
output
mirror
eth
ip
output
mirror
Expected order:
Possible order:

## Slide 33: Results - Action time
packet-per-sec: 1000
duration: 10s

## Slide 34: Results - Action time
frame size: 1024 bytes
packet-per-sec: 1000
duration: 10s
actions: [ip_src, ip_dst, eth_src, eth_dst, udp_src, udp_dst]

## Slide 35: Results - Action time - White box
Tool: ftrace
tracer: function_graph
function: set_ip_addr
frame size: 1024 bytes
packet-per-sec: 1000
duration: 10s
actions: [ip_src, ip_dst]
End-to-end | ours | white box
315 us | 2~3 us | 0.6~0.8us

## Slide 36: Result - Buffer size
Buffer size (byte) |  |  |  |  | 
frame size | ovs | pica8 P-3290 | pica8 P-3297 | Edge-core | Centec V350
64 | 16384 | 8256 | 16192 | 32768 | 342464
128 | N/A | N/A | N/A | N/A | N/A
256 | N/A | N/A | N/A | N/A | N/A
512 | N/A | N/A | N/A | N/A | N/A
1024 | N/A | N/A | N/A | N/A | N/A
TX rate: 1Gbps
duration: 5~10s
CVE-2016-2074 [15], buffer overflow

## Slide 37: Results - Busy ratio
duration: 5~10s
Open vSwitch at 1024Mbps
Loss
Out-of-order
Mismatch

## Slide 38: Results - Pipeline Gain
duration: 5~10s
Open vSwitch at 1024Mbps
Loss
Out-of-order
Mismatch

## Slide 39: Results - Pipeline Gain
2 ports
48 ports
loading | packet operation time | Pipeline gain
↑ | ↑ | ↑

## Slide 40: Result - Timeout Accuracy
Switch | Accidle-timeout | Acchard-timeout
Open vSwitch | 2% | 0%
Pica8 P-3290 | -16.24% | 4.7%
Pica8 P-3297 | 24.64% | 3.3%
Edge-corE AS4610 | 10% | 0%
Centec V350 | 17.64% | 1.66%
hard-timeout: 3~7
idle-timeout: 5
frame size: 64 byte
packet-per-sec: 10000
hard-timeout
idle-timeout
packets
Pica8 switches not reset the timer

## Slide 41: Conclusion
Method evaluation
7 test parameters → 6 insights
The hardware switch have ±20% deviation for idle timeout.
The Packet-in rate for hardware switch is approximately 20 times higher than software switch
The hardware switches reach 40~60% pipeline gain under handling the 1Gbps traffic.
Switch evaluation
Burst traffic and packet modification: Pica8 P-3297
Multi-table handling: Edge-corE AS4610
Issues for switch implementation
Apply-Action
Burst Packet-in → crash
idle-timeout timer not reset properly

## Slide 42: Future Work
Loading
Unconsidered variables: Queuing time
Notes: 目前設計的5個測試方法，都沒有為 loading 說計測試情境，後續可整合 loading 考處其在測試方法中的影響

## Slide 43: Reference
Open Network Foundation. https://www.opennetworking.org/about/onf- overview.
“OpenFlow Switch Specification,” vol. 3, pp. 1–164, 2013.
OFTest. http://www.projectfloodlight.org/oftest/.
Ryu certification. https://osrg.github.io/ryu/certification.html.
Spirent, “OpenFlow Performance Testing,” 2015.
C. Rotsos, N. Sarrar, S. Uhlig, R.Sherwood, and A. W. Moore, “OFLOPS:An open framework for OpenFlow switch evaluation,” Lecture Notes in Computer Science (including subseries Lecture Notes in Artificial Intelligence and Lecture Notes in Bioinformatics), vol. 7192 LNCS, pp. 85–95, 2012.
A. Bianco, R. Birke, L. Giraudo, and M. Palacin, “OpenFlow switching: Data plane per- formance,” IEEE International Conference on Communications, 2010.
P. Emmerich, D. Raumer, F. Wohlfart, and G. Carle, “Performance characteristics of virtual switching,” 2014 IEEE 3rd International Conference on Cloud Networking, CloudNet 2014, pp. 120–125, 2014.

## Slide 44: Reference
A. Gelberger, N. Yemini, and R. Giladi, “Performance analysis of Software-Defined Networking (SDN),” in Proceedings - IEEE Computer Society’s Annual International Symposium on Modeling, Analysis, and Simulation of Computer and Telecommunications Systems, MASCOTS, pp. 389–393, 2013.
M. Jarschel, S. Oechsner, D. Schlosser, R. Pries, S. Goll, and P. Tran-Gia, “Modeling and performance evaluation of an OpenFlow architecture,” 2011 23rd International Teletraffic Congress (ITC), pp. 1–7, 2011.
C. Rotsos, G. Antichi, M. Bruyere, P. Owezarski, and A. W. Moore, “OFLOPS-Turbo: Testing the next-generation OpenFlow switch,” IEEE International Conference on Communications, pp. 5571–5576, 2015.
R. B. Handfield and K. Mccormack, “What You Need to Know About SDN Flow Tables,” Supply Chain Management Review, no. September, pp. 29–36, 2015.
V. Tanyingyong, M. Hidell, and P. Sjödin, “Improving PC-based OpenFlow switching performance,” Architectures for Networking and Communications Systems (ANCS), 2010 ACM/IEEE Symposium on, pp. 8–9, 2010.
D. Y. Huang, K. Yocum, and A. C. Snoeren, “High-fidelity switch models for software- defined network emulation,” Proceedings of the second ACM SIGCOMM workshop on Hot topics in software defined networking - HotSDN ’13, p. 43, 2013.
CVE-2016-2074: MPLS buffer overflow vulnerabilities in Open vSwitch. http://openvswitch.org/pipermail/announce/2016-March/000082.html.